## Slide 1
1-Bit Adders

## Slide 2
Types of carry propagate adders (CPAs):
  Ripple-carry (slow)
  Carry-lookahead (CLA) (fast)
  Prefix (faster)
Carry-lookahead and prefix adders faster for large adders but require more hardware
Skipping prefix for the sake of time, but:
  It is similar to carry-lookahead with a prefix tree structure instead of what we’ll see for the CLA
Multi-Bit Adders (CPAs)

## Slide 3
Chain 1-bit adders together
Carry ripples through entire chain
Disadvantage: slow
Ripple-Carry Adder

## Slide 4
Carry-Lookahead Adder
0
1
1
0
Carry-in
Sum
A
B
0
Carry-Out

## Slide 5
Carry-Lookahead Adder
1
1
0
0
Carry-in
Sum
A
B
1
Carry-Out
Generate

## Slide 6
Carry-Lookahead Adder
0
1
0
1
Carry-in
Sum
A
B
1
Carry-Out
Propagate

## Slide 7
Carry-Lookahead Adder
1
1
1
1
Carry-in
Sum
A
B
1
Carry-Out
Generate
Propagate

## Slide 8
Compute Cout for k-bit blocks using generate and propagate signals
Some definitions:
  Column i produces a carry out by either generating a carry out or propagating a carry in to the carry out
  Generate (Gi) and propagate (Pi) signals for each column:
    Generate: Column i will generate a carry out if Ai and Bi are both 1.
  Gi = Ai Bi
    Propagate: Column i will propagate a carry in to the carry out if Ai or Bi is 1.
  Pi = Ai + Bi
    Carry out: The carry out of column i (Ci) is:
  Ci = Ai Bi + (Ai + Bi )Ci-1 = Gi + Pi Ci-1
  Please keep in mind that each of these +’s are for OR and each multiplication is really AND
Carry-Lookahead Adder

## Slide 9
Now use column Propagate and Generate signals to compute Block Propagate and Generate signals for k-bit blocks, i.e.:
  Compute if a k-bit group will propagate a carry in (to the block) to the carry out (of the block)
    This requires a propagate for each individual pair of bits
  Compute if a k-bit group will generate a carry out (of the block)
    This requires at least one generate an individual pair of bits AND propagates for each pair of bits later in the sequence
Block Propagate and Generate

## Slide 10
Example: Block propagate and generate signals for 4-bit blocks (P3:0 and G3:0): Gi = Ai Bi Pi = Ai + Bi
  P3:0 = P3P2 P1P0
  G3:0 = G3 + P3 (G2 + P2 (G1 + P1G0 )
  C3 = G3:0 + P3:0 Cin
Generally,
  Pi:j = PiPi-1…. Pj+1Pj
  Gi:j = Gi + Pi (Gi-1 + Pi-1 (Gi-2 + Pi-2Gi-3… )
  Ci = Gi:j + Pi:j Cj-1
Block Propagate and Generate Signals

## Slide 11
32-bit CLA with 4-bit Blocks
  P3:0 = P3P2 P1P0
  G3:0 = G3 + P3 (G2 + P2 (G1 + P1G0 )
  Cout = C3 = G3:0 + P3:0 Cin

## Slide 12
Selects between one of N inputs to connect to output
Example:
Multiplexer (Mux)
2:1 Mux

## Slide 13
Using mux as a lookup table to replicate a logic gate of some kind:
Logic Applications using Multiplexers

## Slide 14
The “under the hood” logic for a multiplexer would look like this for a 4:1 and 2:1 MUX respectively:
Therefore, we want to reduce the size of the MUX when we can!
Multiplexer (Mux)

## Slide 15
Reducing the size of the mux
Logic Applications using Multiplexers

## Slide 16
Logic using Multiplexers
For the following function
Show the truth table
Draw circuit using a combination of 4:1 and 2:1 multiplexers. You must use at least one multiplexer but may also include other logic gates as well as a ground signal (constant 0 input) and voltage (constant 1 input) as needed.

## Slide 17
Logic using Multiplexers

## Slide 18
Logic using Multiplexers

## Slide 19
ALU: Arithmetic Logic Unit
ALUControl1:0 | Function
00 | Add
01 | Subtract
10 | AND
11 | OR
Example: Perform any of them

## Slide 20
Flag | Description
N | Result is Negative
Z | Result is Zero
C | Adder produces Carry out
V | Adder oVerflowed
ALU with Status Flags

## Slide 21
ALU with Status Flags

## Slide 22
Some helpful course pages
https://hardcaml-mini-course-at-stevens.github.io/hardcaml-docs/designing-circuits/combinational_logic
https://hardcaml-mini-course-at-stevens.github.io/hardcaml-docs/designing-circuits/mux4
https://hardcaml-mini-course-at-stevens.github.io/hardcaml-docs/designing-circuits/alu